## Slide 1
Correct energy demand, according with equipment efficiency
Calculate minimum power to be provided from PV panels, according with weather information and standard electrical losses
Define arrangement of PV panels in series and parallel
From the House:
Load curve
Peak power (W)
Energy demand (kWh/day)
Outlet AC voltage (V)
Design assumptions:
Battery autonomy (h)
Battery DOD and SOC
DC bus voltage (V)
Calculate energy demand from batteries
Check electrical compatibility between the charge controller and the adopted DC bus voltage
Calculate the minimum energy from DC-bus
Calculate the battery bank capacity
ix - Define arrangement of batteries in series and parallel
Check electrical compatibility: minimum current produced from panels and the charge controller current
Check electrical compatibility between DC inverter voltage and DC bus voltage
Define PV panels config.
Define charge controller
Define batteries
i - Correct energy demand, according with equipment efficiency
ii - Calculate minimum power to be provided from PV panels, according with weather information and standard electrical losses
iii - Define arrangement of PV panels in series and parallel
Weather information from local:
Solar irradiation/ insolation
Field temperature
Each equipment item from PV system:
detailed datasheet information
vi - Calculate energy demand from batteries
x - Check electrical compatibility between the charge controller and the adopted DC bus voltage
vii - Calculate the minimum energy from DC-bus
viii - Calculate the battery bank capacity
xi - Correct temperature from PV panels to the ambient temperature
xii - Check electrical compatibility: minimum current produced from panels and the charge controller current
xiv - Check electrical compatibility among inverter and other equipment or house requirements
Define PV panels config.
Define charge controller
Define batteries
Define inverter
Pick panel, inverter, controller and battery candidates
Inputs
iv - Calculate the minimum current and voltage supplied from the PV panels to the charge controller
v - Check electrical compatibility between PV panels arrangement and charge controller
xiii - Define number of charge controllers

## Slide 2
Correct energy demand, according with equipment efficiency
Calculate minimum power to be provided from PV panels, according with weather information and standard electrical losses
Define arrangement of PV panels in series and parallel
From the House:
Load curve/Day
Peak power (W)
Energy demand (kWh/Day)
Outlet AC voltage
Assumptions:
Battery autonomy (h)
DC bus voltage (V)
Weather information:
solar irradiation/ insolation (local)
Each equipment item:
detailed datasheet information
Check electrical compatibility between PV panels arrangement and charge controller
Calculate energy demand from batteries
Check electrical compatibility between the charge controller and the adopted DC bus voltage
Calculate the minimum energy from DC-bus
Calculate the battery bank capacity
Define arrangement of batteries in series and parallel
Check electrical compatibility: minimum current produced from panels and the charge controller current
Define number of charge controllers
Check electrical compatibility between DC inverter voltage and DC bus voltage
Check electrical compatibility between AC inverter output with the house outlet AC voltage
Check electrical compatibility between minimum inverter power output and house' s peak demand
Define PV panels config.
Define charge controller
Define batteries
Define inverter
Pick panel, inverter, controller and battery candidates